ALLTRAX DCX Motor Controller Electrical Specifications

Separately Excited DC motor controller

Model:                                       			DCX 4834 / 4844   ( -ET for Elec-Trak version )

Armature Current Limit, 2 minutes:           	         300A / 400A

Armature Current, 5 minutes:                 		         150A / 210A

Armature Current, I hour:                    		         135A/ 160A

Field Current Limit:                         		30A    ( 3A for ET version )

Battery Input Voltage:                       		24 - 48VDC Nominal, 6OVDC max

Undervoltage cutback:                        		adjustable, 16-30 VDC

Overvoltage shutdown:                        		adjustable, 30-60 VDC

Operating Frequency:                         		18 kHz

Key, Throttle and Reverse inputs:     		12 - 60 VDC, 15mA max

Contactor drive current:                     		2A sink max

Reverse Horn Output:                           		5OmA sink max

Standby Current:                               		< 35mA

Throttle Input:                                		ITS (inductive),  0-5K,  5K-0  Ohm +/-10%

Operating Temperature:                         		-25C to 75C,   shutdown at 95C

Software adjustable features;

Throttle acceleration / deceleration rate - user

Armature current limit - user

Brake current limit - user

Under / Over voltage shutdown - user

Top Speed & Turbo button - user

Programmable Field Map - factory

Half speed reverse – factory  ( half speed reverse disabled for ET model unless requested by user )

ALLTRAX Inc.

1111 Cheney Creek Rd.

Grants Pass, OR 97527

www.alltraxinc.com

ph: 541-476-3565

fax: 541-476-3566

rev B 2-11-04